## Slide 1: RECENT EFFORTS TOWARDS EFFICIENT AND SCALABLE NEURAL WAVEFORM CODING
Kai Zhen
Ph.D. Candidate in Computer Science and Cognitive Science
Research Committee:
Minje Kim, Robert Goldstone, Donald Williamson, Shen Yi

## Slide 2: Acoustic Signal Processing in Intelligent Systems
s

## Slide 3: Speech/Audio Coding in One Slide

## Slide 4: The Opportunity, Challenge, and Approach
Bridge the gap between machine learning and DSP
  DSP
    Pre-emphasis
    Linear predictive coding (LPC)
    Perceptual weighting
    Residual coding
  Machine learning
    End-to-end speech coding neural network [1]
    Residual learning
    Soft-to-hard quantization [2]
    Sub-pixel upsampling network [3]
Lightweight
  Oops, my phone battery is drained after decoding a high quality audio message…
Scalability
  Need to support various bitrates: from ~9kbps to ~24kbps

## Slide 5: The Structure of the Talk
Neural Quantization
Cross-Module Residual Learning
Perceptual Loss

## Slide 6: The Structure of the Talk
Neural Quantization
Conventional DSP Techniques
Perceptual Loss
Multistage vector quantization
Linear predictive coding
Human auditory perception
Soft-to-hard quantization
Cross-module residual learning
Collaborative quantization
Discrepancy in metrics
Psychoacoustical calibration

## Slide 7: The Structure of the Talk
Neural Quantization
Conventional DSP Techniques
Perceptual Loss
Multistage vector quantization
Linear predictive coding
Human auditory perception
Soft-to-hard quantization
Cross-module residual learning
Collaborative quantization
Discrepancy in metrics
Psychoacoustical calibration

## Slide 8: Neural Scalar Quantization
Why is autoencoder itself not enough?
Autoencoder reduces the size of the feature map
The encoder part of each AE still produces real-valued vectors
Without quantization, each real value is still represented by a 16-bit floating-point.
Jjhhhhh/
Sub-pixel
Bottleneck CNN
Bottleneck CNN
Sub-pixel
Quantizer
Stride 2
Bottleneck CNN
Bottleneck CNN
Stride 2
Hoffman coding,
bitstream transmission

## Slide 9: Neural Scalar Quantization
How about conducting a clustering analysis?
K-means clustering with 128 kernels
  Each real value from the encoder output will be represented by the closest kernel out of 128 candidates
  It suffices to use not 16 bits but 8 bits to represent each real value.
  2X more compression!
But, a clustering algorithm has no control over the kernel probabilities
  If kernels are with highly uneven probabilities, the data can be further compressed through entropy coding!
Jjhhhhh/
Sub-pixel
Bottleneck CNN
Bottleneck CNN
Sub-pixel
Quantizer
Stride 2
Bottleneck CNN
Bottleneck CNN
Stride 2
Hoffman coding,
bitstream transmission

## Slide 10: Neural Scalar Quantization
A trainable K-means clustering style quantization
The encoder part of each AE produces a real-valued vector
Soft-to-hard quantization is to convert it into a bitstring
The coding gain depends on the distribution of the code
Soft-to-hard quantization controls the entropy of the code distribution as a regularization term during optimization
Hard Assignment (Test Time)
Soft Assignment (Training Time)
(Test Time)
(Training Time)

## Slide 11: Neural Scalar Quantization
Soft-to-hard quantization
The encoder part of each AE produces a real-valued vector
Soft-to-hard quantization is to convert it into a bitstring
The coding gain depends on the distribution of the code
Soft-to-hard quantization controls the entropy of the code distribution as a regularization term during optimization
Hard Assignment (Test Time)
Soft Assignment (Training Time)
(Test Time)
(Training Time)

## Slide 12: Speech Coding Versus Audio Coding
Generative speech models versus psychoacoustics
Bitrate
Subjective Quality
Excellent
Good
Normal
Poor
Bad
G.729
AMR
AMR-WB
AMR-WB+
HE-AAC V2
HE-AAC
AAC
MPEG-2 BC
MPEG-1
10k
24k

## Slide 13: Cross-Module Residual Learning
Overview
So, does it work?
Interspeech 2019
The 1st module
Encoder
Decoder
Code Layer
Encoder
Decoder
Code Layer
The 2nd module
Residual signal
Encoder
Decoder
Code Layer
The Nth module
Residual signal
BP for
BP for
BP for

## Slide 14: Background
Cross-Module Residual Learning
The baseline CMRL architecture
Jjhhhhh/
Sub-pixel
Bottleneck CNN
Bottleneck CNN
Sub-pixel
Softmax quantizer
Stride 2
Bottleneck CNN
Bottleneck CNN
Stride 2
Hoffman coding,
bitstream transmission

## Slide 15: Cross-Module Residual Learning
The fully-convolutional architecture
S. Kankanahalli, “End-to-end optimized speech coding with deep neural network,” ICASSP 2018; Interspeech 2019
512X1
x2
x2
Sub-pixel convolution (Upsampling)
512X1
512X100
512X20
512X20
512X100
256X100
Downsampling
Quantization & Huffman coding
9X1X100
9X100X20
9X20X20
9X20X100
9X100X100
256X20
9X100X20
256X20
9X20X20
256X100
9X20X100
256X1
The code vector
9X100X1
512X50
x2
256X100
256X20
256X20
256X100
256X1
256X100
Stride=2
Interlacing two feature maps (256X2) to build one map of 512
x2
512X20
512X20
512X50
512X1
Identity shortcut
Identity shortcut
Identity shortcut
Identity shortcut

## Slide 16: The Take Away from CMRL
The solution from multiple lightweight models can be better than that from a big one with the combined complexity.
The 1st module
Encoder
Decoder
Code Layer
Encoder
Decoder
Code Layer
The 2nd module
Residual signal
Encoder
Decoder
Code Layer
The Nth module
Residual signal
BP for
BP for
BP for

## Slide 17: Don’t Throw DSP Out with the Bathwater
Why model the the entire speech with DNNs?
In source-filter model, the speech production process contains
  Sources
    glottal source, aspiration source, frication source, and transient source
  Filter
    The response of the vocal tract
https://ocw.mit.edu/courses/linguistics-and-philosophy/24-915-linguistic-phonetics-fall-2015/lecture-notes/MIT24_915F15_lec4.pdf

## Slide 18: Linear Predictive Coding
LPC models the vocal tract response
With Levinson-Durbin algorithm, the spectral envelope is estimated with very few amount of bits,
Of course, the estimation is not perfect; the “error” is called the LPC residual.
C. I. Byrnes, P. Enqvist, A. Lindquist, Identifiability And Well-Posedness Of Shaping-Filter Parameterizations: A Global Analysis Approach

## Slide 19: LPC in Coding Systems
s
T. Moriya, et al, Progress in LPC-based frequency-domain audio coding

## Slide 20: An Easy Incremental Work?
Cross-Module Residual Learning
Cross-module residual learning (CMRL)
  CMRL opened a new possibility of introducing residual coding to neural speech coding
  It showed superior performance by concatenating multiple autoencoding modules as a chain of residual coding
  More importantly, it turned out that having an LPC analysis-synthesis block as the 0-th module is effective
The 0-th LPC module
  Learns the spectral envelope (formant information)
  Borrow the LPC module from AMR-WB
  Deterministic (not learnable)
Our goal in the proposed collaborative quantization (CQ) is to harmonize LPC as a learnable block, at least the quantization part
The CMRL architecture

## Slide 21: Collaborative Quantization
A trainable quantization scheme for LPC coefficients
the criterion used for the computation and quantization of the LPC parameters is minimization of the residual signal energy
C. I. Byrnes, P. Enqvist, A. Lindquist, Identifiability And Well-Posedness Of Shaping-Filter Parameterizations: A Global Analysis Approach
High-pass filter
Pre-emphasis filter
Calculate LPC coefficients
LPC coefficients quantization
Calculate LPC residuals
Coded LPC
Coefficients
(regularization)
Raw waveform
Residual waveform

## Slide 22: Cross-Module Residual Learning
Audio demo
fasw/sa1.wav
ICASSP 2020; http://www.kaizhen.us/speechcoding.html
Bitrate (kbps) | Reference | AMR-WB | OPUS | LPC+CMRL | LPC+CMLR +CQ
~9 |  |  |  |  | 
~9 |  |  |  |  | 
~24 |  |  |  |  | 
~24 |  |  |  |  | 

## Slide 23: Performance
CQ improves the CMRL baseline in the low bitrates
CQ shows decent performance in the high bitrates
PESQ and MUSHRA
CQ shows reasonably better PESQ scores
Model complexity
PESQ

## Slide 24: The Structure of the Talk
Neural Quantization
Conventional DSP Techniques
Perceptual Loss
Multistage vector quantization
Linear predictive coding
Human auditory perception
Soft-to-hard quantization
Cross-module residual learning
Collaborative quantization
Discrepancy in metrics
Psychoacoustical calibration

## Slide 25: Objective Measures Do NOT Align
s
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
Actual mean opinion scores (MOS) for non-speech audio signals

## Slide 26: Masking Effects from Psychoacoustics
s
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
Actual mean opinion scores (MOS) for non-speech audio signals

## Slide 27: The Usage of the Masking Threshold in DNNs
Priority weighting
s
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
Actual mean opinion scores (MOS) for non-speech audio signals

## Slide 28: The Usage of the Masking Threshold in DNNs
Noise Modulaiton
s
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
Actual mean opinion scores (MOS) for non-speech audio signals

## Slide 29: The Usage of the Masking Threshold in DNNs
MUSHRA results
ssssss
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
sssss

## Slide 30: The Usage of the Masking Threshold in DNNs
Noise Modulaiton
s
S. W. Fu, et al, End-to-End Waveform Utterance Enhancement for Direct Evaluation Metrics Optimization by Fully Convolutional Neural Networks
Bitrate (kbps) | Reference | AMR-WB | OPUS | LPC+CMRL | LPC+CMLR +CQ
~9 |  |  |  |  | 
~9 |  |  |  |  | 
~24 |  |  |  |  | 
~24 |  |  |  |  | 

## Slide 31: The Structure of the Talk
Neural Quantization
Conventional DSP Techniques
Perceptual Loss
Multistage vector quantization
Linear predictive coding
Human auditory perception
Soft-to-hard quantization
Cross-module residual learning
Collaborative quantization
Discrepancy in metrics
Psychoacoustical calibration

## Slide 32: - law companding
Compress and expand the bit depth
Scenario
  Transmitting a telephone audio signal
  Compress the bit-depth from 16-bit to 8-bit per sample
  Expand the bit-depth from 8-bit to 16-bit per sample
If it is linearly companded,
  The amount of quantization error for samples with small amplitudes is the same with that for high-amplitude ones.
  All samples with the amplitude from 0 to 255 will be rounded down to 0.
Notes: >>> 32120/256
125
>>> 125*256
32000

## Slide 33: - law companding
More quantization levels for smaller values
Compression
  mu(33/32768) = 0.0412;
  floor(128*0.0412) = 5;
Expansion
  mu_inv(5/128) = .00094846
  ceil(32768* .00094846) = 32

## Slide 34: - law companding
Can it be used to weigh the MSE loss term?
Interestingly, the kernels “learned” from our neural quantizer reflect the flavor of - law companding
  More quantization levels for smaller values.
Rethink the mean-squared error
  The data:
  The estimate-1:
  The estimate-2:
  Equivalent MSE, but should they be considered the same?
Distribution of 32 learned
quantization bins in the AE modules

## Slide 35: Wave-U-Net Quantization
Can a Wave-U-Net be used for coding?
A plain autoencoder with identical shortcuts
Popular for image segmentation, audio separation, speech enhancement, etc.
Have been used in audio coding, but
Add/Concat
Add/Concat
Add/Concat

## Slide 36: Wave-U-Net Quantization
From identical shortcuts to approximated shortcuts
More observations can be acquired from empirical results
  May not need the bottleneck
  Dynamic bit allocation for identical shortcuts
    Less bits for the one near the bottleneck
    May not even need to quantize all shortcuts
1
1
2
2
3
3

## Slide 37: Wave-U-Net Quantization
From scalar quantization to vector quantization
The current Softmax quantiztion is scalar-based
  Temporal pattern not utilized
How about a trainable VQ
  The code is just the index
A. V. D. Oord, et al, Neural Discrete Representation Learning
Embedding dictionary
Calculate the distance
argmin
Get the index
Embedding dictionary
Hard Assignment (Test Time)
Soft Assignment (Training Time)
(Test Time)
(Training Time)

## Slide 38: Cross-Module Residual Learning
Soft-to-hard quantization and the loss function
Time-domain sample-by-sample reconstruction
  May not be the best
Spectral reconstruction
  In the mel-scale
Entropy loss
  Reducing entropy of the code can increase the coding gain
  Original bitrate: (256*5)*16000/(512-32)+2400 = 45kbps
    Huffman codding reduces the bitrate further
Interspeech 2019
Hard Assignment (Test Time)
Soft Assignment (Training Time)
(Test Time)
(Training Time)
(Normalized soft count)

## Slide 39: Collaborative Quantization
A trainable quantization scheme for LPC coefficients
In CMRL the LPC module from AMR-WB consumes 2.4kbpsWe want to do it better
Trainable LPC?
  Too easy to estimate
But, quantization is a learnable part in neural coding!
ICASSP 2020
6.45kbps
2.4kbps
27%
Distribution of 32 learned quantization bins in the CMRL AE modules
Spikiness controlled by the entropy loss
High-pass filter
Speech Signal
Pre-emphasis filter
Calculate LPC coefficients
LPC coefficients quantization
Calculate LPC residuals
Residual Frame
Coded LPC
Coefficients
(regularization)

## Slide 40: Background
Soft-to-hard quantization
The encoder part of each AE produces a real-valued vector
Soft-to-hard quantization is to convert it into a bitstring
The coding gain depends on the distribution of the code
Soft-to-hard quantization controls the entropy of the code distribution as a regularization term during optimization
Hard Assignment (Test Time)
Soft Assignment (Training Time)
(Test Time)
(Training Time)

## Slide 41: Background
The LPC module
We implement a basic LPC module in TensorFlow
There are some implementation details about the choice of the windows
High-pass filter
Speech Signal
Pre-emphasis filter
Calculate LPC coefficients
LPC coefficients quantization
Calculate LPC residuals
Residual Frame
Coded LPC
Coefficients
(regularization)

## Slide 42: Trainable LPC Quantization
Soft-to-hard quantization for LPC coefficients
Soft-to-hard quantization adjusts the distribution of the codes to maximize the coding gain
Histogram of initial 16 LPC coefficients
Distribution of 32 learned
quantization bins in the AE modules
Entropy regularization

## Slide 43: Overview of the CQ system
Trainable LPC quantization + CMRL

## Slide 44: Collaborative Quantization
MUSHRA
Complexity
CQ improves the CMRL baseline in the low bitrates
CQ shows decent performance in the high bitrates
ICASSP 2020
Reference
LPC-CMRL 16 kbps
CQ 9 kbps
AMR-WB 8.85 kbps
LPC-CMRL 9 kbps
OPUS 9 kbps
Anchor (4kHz )
0
20
40
60
80
100
Reference
CQ 24 kbps
LPC-CMRL 24 kbps
OPUS 24 kbps
AMR-WB 23.85 kbps
Anchor (4kHz )
0
20
40
60
80
100